## Slide 1
W04
Sinusoidal Steady State
Sinusoidal Source Term and Systems Approach
IKCU\Mechatronics Engineering\MEE303 Sensor Systems

## Slide 2
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Alternating Voltage or Current
A DC voltage or current has a fixed magnitude (amplitude) and a definite direction associated with it. For example, +12V represents 12 volts in the positive direction, or -5V represents 5 volts in the negative direction.
An alternating function or AC Waveform on the other hand is a"Bi-directional" waveform.
An AC waveform is
  constantly changing its polarity every half cycle
  alternating between a positive maximum value and a negative maximum value
  respectively with regards to time
Why it is an Alternating
The periodic or AC waveform is a result of the rotating electrical generator.

## Slide 3
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
AC Waveform Charteristics
Vavg : (Full Rectified) Average Voltage, average value of the signal assuming that both of the peaks are positive sided. [V]
Instantaneous Voltage : Terminal voltage at any time instant t after any zero crossing. To estimate the voltage value, the t ime instant should be converted to angle. It can be done using angular frequency (or rotating speed of rotor).
f: Frequency or oscillation of a signal is the value of repetition observed in a changing signal in unit time (per second) [Hz]
Amplitude (A)=Vmax [V]
Vrms : Effective Value of the signal [V]
RMS Value Calculation
Average Value Calculation

## Slide 4
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
AC Waveform Charteristics
Average Value Calculation
The value of an AC voltage is continually changing from zero up to the positive peak, through zero to the negative peak and back to zero again. Clearly for most of the time it is less than the peak voltage, so this is not a good measure of its real effect
The RMS value is the effective value of a varying voltage or current. It is the equivalent steady DC (constant) value which gives the same effect.
RMS Value Calculation
Thus one way to determine a quantitative measurement size is to use the average rectified value which can be computed by averaging the absolute value of a waveform over one full period of the waveform
The average of a symmetric alternating value is zero.

## Slide 5
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Euler Formula
establishes the fundamental relationship between the trigonometric functions and the complex exponential function
Phasor
A phasor is a complex number representing a sinusoidal function whose amplitude, angular frequency, and initial phase are time-invariant.
The projection of a rotating vector around origin y axis in cartesian coordinate system is a sine function so it can represent a sinusoidal (alternating) source (voltage or curent)
  The length (or the radius) of the rotating vector is the amplitude of alternating voltage/current
  The angle between the vector and the horizantal axis is the phase value (θ).
  The angular velocity of this rotating vector is the angular frequency of alternating voltage/current.
The Sinusoidal Waveform of AC Network of Turkey

## Slide 6
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Phase
Phase is defined a particular stage or state of a periodic phenomenon. If this particular taken as a begining then three phase alternatives can exist
The phase of a Sinusoidal Waveform is the angle Φ (Greek letter Phi), in degrees or radians that the waveform has shifted from a certain reference point along the horizontal zero axis.
The phase is caluclated by
  first the lead or lag time of signal to reach zero magnitude with positive derivative value (with trend of increase)
  And after calculating the phase angle using mesaured time.

## Slide 7
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Comparing two atlernating circuit variables
Comparing amplitudes
Phasors are useful
Comparing phases
Phasors are useful

## Slide 8
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Comparing two atlernating circuit variables
An important point in operations of two time dependent signals is whether they are synchronized or not.
For electrical definitions, two voltage signals or two corrent signals or one voltage with one current signals either can be synchronized or have a phase diference.
If two signals are synchronized, they both pass the zero points and the maximum value points at the same time.
If two signals pass the zero points and maximum value points in different moments then a phase shift occurs.
Phase shift is 90 when the reference signal is B.
Phase shift is 90 when the reference signal is A.
Phase shift is -90 when the reference signal is B.
Phase shift is zero . Therefore, two signals are in phase

## Slide 9
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Phase is 45 from B to A
the waveforms are frozen at time t = 30o, the corresponding phasor diagram would look like the one shown on the right.
the current phasor lags behind the voltage phasor
the voltage phasor leads the current phasor

## Slide 10
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN

## Slide 11
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Phasors as complex numbers
The voltage by a combination of AC current/voltage sources connected to the same circuit is determined by vector addition and subtraction operations.
Two dimensional vectors can also be represented via complex numbers

## Slide 12
Passive Components reaction to Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Resistor (R)
Ohm’s Law can be used for resistance under the influence of alternating voltage.
According to equations above, there is no phase shift between current and voltage on a resistor.
Nevertheles, the amplitude changes due to Ohm’s Law.
AC power dissipated on resistor is:

## Slide 13
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
İnductor (Coil)
Passive Components reaction to Sinusoidal Input
In contrast with resistors, coils under alternating voltage resists against alternating current. The voltage on a coil (the voltage measured between two terminals) can be calculated using Lenz Law.
If this equation is studied considering the alternating current, the relationship between the current and voltage might be predicted
The phase shift results with negative electrical power. Negative power denotes that the coil transfer power to the circuit.
The ‘resistance’ of coils changes due to frequency. This is called as reactance (inductive reactance XL) for this reason.
This result shows us that there is a 90 degrees of phase shift between voltage and current on a coil under AC. The voltage leads current by phase angle of 90 degree

## Slide 14
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Inductive Reactance
Passive Components reaction to Sinusoidal Input Examples
The ‘resistance’ of coils changes due to frequency. This is called as reactance (inductive reactance XL) for this reason.
Ohm’s Law might be implemented easily to alternating current circuits using quantity, the reactance. In that case, the calculations should be made using complex numbers instead of scalars.

## Slide 15
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Passive Components reaction to Sinusoidal Input
Capacitor (C) (Capacitance)
Capacitors react different due to the voltage level applied to them under alternating current.
If the voltage level applied is greater than the voltage on a capacitor, the source charges the capacitor; in opposite case, capacitor behaves like a source. And discharges through the circuit elements.
The current equation for a capacitor is:
The phase difference between voltage and current is 90 degrees on a capacitor or in other words, current leads voltage 90 degrees.
This case results with negative electrical power which means that capacitor transfers power to the circuit (i.e. Capacitor discharges its electrical charge).
The ‘resistance’ of the capacitors change due to the frequency of the alternating voltage.The higher frequency of the AC signal, the more easily that signal will pass through the capacitor. Thus, this is called as capacitive reactance, Xc.

## Slide 16
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Capacitor (C) (Capacitance)
The current of the AC source leads the voltage of the source 90 degrees. The resistance effect of the capacitor to AC source is calculated considering this.

## Slide 17
Sinusoidal Input
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
Resistor, Reactance and Impedance
The resistance against the current can be in three types:
Resistance: It is the friction of electrons during motion. Its symbol is “R” and unit is [] (i.e. [Ohm]). It does not form any phase shift.
Reactance: It is the inertia of electrons. It occurs if there is a change in voltage or current values (if an electric or magnetic field occurs). The capacitor and inductor are the main circuit components which this influence is highly distinct.
If there is a reactance effect in a circuit, there is also phase shift. If the component is a capacitor, the current leads voltage by 90 degrees whereas if it is an inductance, the current lags voltage by 90 degrees.
Impedance, is the strain against the current in an electrical circuit. Impedance is the total resistance and reactance effects of all components. The resistance in DC circuits is the impedance in AC’s
The AC implemented Ohm’s Law can be seen as below. Please consider that all the quantities are in complex number form in the equation below :
Like Ohm’s Law, other laws (Kirrschoff’s, grid theorems, etc.) used in circuit analysis can be also implemented in AC in condition of using complex numbers.
Ohm’s Law via Impedance

## Slide 18
AC Circuit Analysis
IKCU\Mechatronics Engineering\MEE212 Electric Circuits Dr.Levent ÇETİN
1. Frequency Transfer Function Method
G(s)
F(s)
X(s)
Assuming all initial conditions are zero
Find the transfer function
Set s=jw and find F(jw) which is complex function
Convert Cartesian form to polar form using formulas
Find the steady state sinusoidal function with given formula